## Slide 1
General Map
CM X32 (32)
AES50 A
AES50 A
DL 16 #1
AES50 B
AES50 A
DL 16 #2
AES50 B
AES50 A
DL 16 #3
AES50 B
AES50 B
AES50 B
LJ WING Rack 1
AES50 A
USB (128) to/from REAPER Merged via VB Audio Matrix Coconut software 512 samples.
WINGUSB (1-48)
AES50 C
REAPER Stem Record & Playback PC
KTUSB (48)/USB Extender if needed
DN 9630
AES50
AES50 B (49-96)
LJ WING Rack 2
AES50 A
Recoding/Playback Notes:
To record into REAPER:
  X32 routing inputs should be userin 1-32 (record setup)
  WING inputs should be MAIN choices
To PLAY from REAPER:
  X32 routing inputs should be AES50 B 1-32 (play setup)
  WING inputs should be ALT choices (USB)
Assignments VB Audio Matrix Coconut
  Wing USB 1-48 -> Virtual 1-48-> REAPER 1-48 -> Virtual 1-48 -> Wing USB 1-48
  KT USB 1-48 -> Virtual 49-96 -> REAPER 49-96 -> KT USB 1-48
  XLIVE USB 1-32 -> Virtual 97-128 -> REAPER 97-128 -> XLIVE USB 1-32
XLIVE USB (97-128)
Local Ins for mics/fx
Local Ins for mics
Local Outs for Monitors
Local Outs Mains/Subs/fx
4 in 4 out ext fx
Rev 20260515a
AOut 1-8=Out 1-8
AOut 9-16=Out 9-16
BOut 1-48=UsrOut1=48
AES50 C
AES50 A
DL 16
AES50 B
1-6
AES50 A
DL 16
AES50 B

## Slide 2
WING 1
WING2
CM X32
Vocal Channels
Bus 01 VOX
Bus 02 vvrb1
Bus 03 vvrb2
Instr Channels
Bus 04 Inst
Bus 05 ivrb1
Bus 06 ivrb2
Any Channel
Bus 07 mon 1 OvrChr
Bus 08 mon 2 Piano
Bus 09 mon 3 Organ
Bus 10 mon 4 Guitar
Bus 11 mon 5 Vocal
Bus 12 mon 6 Drum
C43 out
C44 out
C45 out
C46 out
C47 out
C48 out
C43 in
C44 in
C45 in
C46 in
C47 in
C48 in
chAUX1
chAUX2
chAUX3
chAUX4
chAUX5
chAUX6
Bus 07
Bus 08
Bus 09
Bus 10
Bus 11
Bus 12
Any Channel
Lcl Out 1
Lcl Out 2
Lcl Out 3
Lcl Out 4
Lcl Out 5
Lcl Out 6
C43 out
C44 out
C45 out
C46 out
C47 out
C48 out
C43 in
C44 in
C45 in
C46 in
C47 in
C48 in
B43 in
B44 in
B45 in
B46 in
B47 in
B48 in
Matrix 1 Main LR
Matrix 2 Main C
Matrix 4 Record LR
Matrix 3 SUB
B39/40 out
B41 out
B42 out
B39/40 in
B41 in
B42 in
Vocal
Channels
Instr
Channels
Bus 01 VOX
Bus 02 vvrb1
Bus 03 vvrb2
Bus 04 Inst
Bus 05 ivrb1
Bus 06 ivrb2
chAUX1
chAUX2
chAUX3
chAUX4
chAUX5
chAUX6
C31/32 in
C33/34 in
C35/36 in
C37/38 in
C39/40 in
C41/42 in
ch 21-userin21
ch 22-userin22
ch 23-userin23
ch 24-userin24
ch 25-userin25
ch 26-userin26
ch 17/18-usrin 17/18 LR
ch 19-userin19 Mono
ch 20-userin20 SUB
Rev 20260515a
Main 1
Vox + vvrb
Main 2
Inst + ivrb
WING1
LJ X32 Rack
WING2
Fixed Routing Map (not shown is recording/playback)
LCL out 05/06
LCL out 07
Lcl out 08
C31/32 out
C33/34out
C35/36 out
C37/38 out
C39/40 out
C41/42 out
B43 out
B44 out
B45 out
B46 out
B47 out
B48 out
WING 1
WING2

## Slide 3
Group 1 Bus 1
Any Ch
Bus 13
Bus 14
Bus 15
Bus 16
Bus 9
Bus 10
Any ch
Out 9:
MAINS Mono
Out 2, Aux 2: Amps Monitor A2 (guitars)
20260515a
Stagebox A has outputs 1-8 from out 1-8
Userin # matches channel #s 1-32
A1-16 out = Out 1-16 (to stage boxes)
B1-48 out = user out 1-48 (to WING 1 B)
Out 1, Aux1: Amps Monitor A1 (organ)
Mtx 5
EQ no sub
Dyn
AUX 5: + out 10 (dly 135ft commons)
Cry Room Mono
Mtx 6
Some low cut, limiting
Out 5/6 LEFT/RT Mains
MTX 1/2
Some EQ, Dyn
Out 15/16: STREAM Stereo
To Stream Interface
MTX 3/4
EQ/Dyn
AUX 4 (& Out 11)
Amp Subwoofer
ROOM ambient
Out 3, Aux 3: Amps Monitor A3 (vocals)
Out 4: (drums)
Fx8a
Fx8b
Insert
Stereo Ultimo
MAIN LR
EQ and Dynamics
to needs
EQ and Dynamics
to needs
Out 7: (piano)
Out 12: Over Choir Spkrs
Bus (11,12)
C
ch Wing Main Mono->BUS 7
ch Wing Main LR >BUS (5/6)
ch Wing SUB BUS 8
Group 2 Bus 2
Group 3 Bus 3
Group 4 Bus 4
Organ Ch
UNET5->usrout45->B45 to Wing
UNET6->usrout46->B46 to Wing
UNET7->usrout47->B47 to Wing
UNET8->usrout48->B48 to Wing
OR can go to Wing as shown below